## Slide 1: Exploring Brain Waves: A Practical Workshop on the Fundamentals of EEG Data Collection and Visualization
Financially supported by Province North Brabant via grant no. C2314216/5277363
Scientifically supported by the department of Cognitive Science and Artificial Intelligence led by Marie Postma.

## Slide 2
Brain and Behavior Lab coordinator at Mindlabs.
​
PhD student in Cognitive Neuropsychology.​
Thesis: Multisensory speech perception.​
Lab activities:
To conduct Behavioral, EEG, Eye tracking studies.
To host a prestigious BCI competition: hackathon.
EEG recorders: G.nautilus, Hybrid black unicorns, Biosemi.
Eye tracker: Eyelink.
The lab started from Spring 2023 under supervision of
Dr. Harm Brouwer & Dr. Myrthe Faber
Faezeh Pourhashemi
s.f.pourhashemi@tilburguniversity.edu

## Slide 3: Today's schedule:
10:50-12:00
  General theory
  Intro to the EEG recording environment (Simulink)
12:00-12:25
  Lunch break
12:30-14:00
  EEG Prep + Practical
  Mini ERP experiment
  Preprocessing EEG signals

## Slide 4: Ali Mousavi smousavi@uvt.nl

## Slide 5: Evy van Weelden e.vanweelden@uvt.nl

## Slide 6: What is EEG?

## Slide 7: The basics
ElectroEncephaloGraphy
Electrical brain activity
  "Brain waves"
Changes in milliseconds
Deze foto van Onbekende auteur is gelicentieerd onder CC BY.

## Slide 8: Background
Let's zoom in...
The brain
Neurons (brain cells)
Synaps – connection between cells

## Slide 9: Background
More neural activity = more electrical charges!
Thus: EEG electrodes detect synchronous electrical charges of groups of neurons...
Your brain generates enough electricity to power a lightbulb!
Release of neurotransmitters, such as dopamine!

## Slide 10: Background
Upper layer of cortex typically densely filled with pyramidal neurons
  oriented perpendicular to the surface of the skull
*dipole = region of positive charge separated from a region of negative charge
(voltage difference can be measured by electrode)

## Slide 11: Interpretation of EEG signals
Frontal lobe - executive functions, decision making
Parietal lobe - spatial processing, (visual) attention, information processing
Temporal lobe - speech, memory
Occipital lobe - visual processing

## Slide 12
Source: the University of Queensland - Queensland Brain Institute

## Slide 13: Interpretation of EEG signals
Decomposing the EEG signal into frequency bands
Raw EEG

## Slide 14: Interpretation of EEG signals
Decomposing the EEG signal into frequency bands
Raw EEG
Busy, active mind
Relaxed, passive attention
Drowsy, inward focused
Sleep
Source: ScienceDirect – Brain Waves

## Slide 15: Interpretation of EEG signals
"Averaging" the EEG signals occuring around a stimulus -> event-related potential (ERP)
stimulus onset

## Slide 16: Purposes
Medical: epilepsy, sleep disorders...
Research: psychiatric disorders, cognition, brain development, social and affective behavior, brain-computer interfaces, and so on...
Neuromarketing, neuroergonomics, etc....

## Slide 17: Examples ...

## Slide 18
Musicians Residente & Bad Bunny synchronize – Dr. Suzanne Dikker (video @ https://www.suzannedikker.net/ )

## Slide 19: Intro to the recording environment (Simulink)

## Slide 20: Things to know before recording
Electrode placement
  10-20 system, proper placement
  Naming, Numbers

## Slide 21: Things to know before recording
Signal Amplification and Impedance
  EEG signals are typically very small in amplitude and require amplification

## Slide 22: Things to know before recording
Signal Amplification and Impedance
  Different kind of electrodes
    Ag/AgCl (silver chloride)
    Dry or Wet

## Slide 23: Things to know before recording
Signal Amplification and Impedance
  Different kind of electrodes
    Passive or Active
      Active has a higher quality
Passive
Active
Passive
Active
A
A
A
A
Wire --> Amplifier
Amplifier --> Wire

## Slide 24: Things to know before recording
Environmental factors:
  External electromagnetic fields, power line noise and Faraday cage
  SNR, signal quality(signal to noise ratio)
  CMRR higher is better (single amplifier)
    (power line voltage presents commonly on both ends of amplifiers; it shouldn't amplify that noise; it should reject it)

## Slide 25: Things to know before recording
Sculp conductivity
  Individual differences
    men, women, baby, age, drinks, etc...
    Skin moisture
    hair thickness
    presence of hair products

## Slide 26: Things to know before recording
Volume conductance
  Cocktail party analogy
  Temporal and spatial resolution
    Comparing EEG with other modalities like fNIRS and fMRI in this regard

## Slide 27: Things to know before recording
Temporal and spatial resolution
  Comparing EEG with other modalities
    fNIRS (functional near-infrared spectroscopy)
    fMRI (functional magnetic resonance imaging)
  Temporal resolution:
    EEG : High (milliseconds)
    fNIRS: Low (1-10 seconds)
    fMRI : Low (1-5 seconds)
  Spatial resolution:
    EEG: Low (several centimeters)
    fNIRS: Low (1-3 centimeters)
    fMRI: High (1-5 millimeters in 3D)
Each have its own pros and cons and they also can be mixed

## Slide 28: EEG Recording Environment
Overview of MATLAB Simulink
  Brief introduction to Matlab Simulink
  Advantages of using Simulink for EEG data processing
    GUI, Visualized, Model based, Integration with Matlab, Extensive Signal Processing Toolbox, Realtime data processing

## Slide 29: EEG Recording Environment
Integration of G.nautilus System with Simulink
  Overview of G.nautilus 32-channel wireless EEG system
  Steps to integrate the G.nautilus system with MATLAB Simulink

## Slide 30: Configuration settings
Basic structure of a Simulink model for EEG recording (Pre-existing)
Visualization of real-time data acquisition in Simulink (Just run)
Important parameter configs before recording:
sampling rate
channel selection
filtering

## Slide 31: Reference and Ground
Mono polar and bipolar :
Shorty mention during the recording
Shortly mention Ground and reference electrodes functionality:
Ground:
  Common return path to close electrical circuit
Reference: (monopolar)
  Stable comparison point for measuring the electric potential
  Each electrode compare itself to the reference
Ground
Reference

## Slide 32: EEG prep + Practical
Creating intentional problems during recording
  How to treat a participant (Explanations, ethics, etc.)
  Participant Comfort and Safety:
    before study ask them to dress comfortably and don’t use hair gels and conditioners... (bring my announcement here)
  Recap the previous session
  Forget to turn amplifier on
  Forget gel on one channel
  Forget ear reference
  Show impedance check and recording settings
  Environmental factors like powerline noise
  Show the data with and without notch filter (at least one channel)
  Show artifacts, muscle movements, blinks
  Alpha waves in rest (closed eyes)
    How we count the alpha band frequency on a grid
    What is the standard range of voltage for EEG?

## Slide 33: ERP experiment
Auditory oddball task
Download link: https://github.com/MindLabs-Tilburg/EEGworkshop [please wait until experiment is over ;) ]
Also download one .set from: https://nemar.org/dataexplorer/detail?dataset_id=ds003061

## Slide 34: Data analysis

## Slide 35: Installing and starting EEGlab
Like adding any toolbox for Matlab

## Slide 36: Outline (It will be projected on the screen while we do it)
Loading and visualizing data before pre-processing
Preprocessing the data
  Filtering
  Re-referencing
  Resampling
Artifact removal
  Eye rejection
  ICA/ automated rejection
    Source understanding
    If you don't have events beware of stationarity in segmenting
Plot data
  Time domain
    features
  Frequency domain
    Features
  Time frequency (if we had time )
Batch analysis and coding in Matlab

## Slide 37: Filtering

## Slide 38: ICA (independent component analysis)
With 7 mics you can separate up to 7 different sources of voice (7 tables)

## Slide 39: ICA (independent component analysis)
Generalize that to a football match, and mass response of fans to a stimuli in the court

## Slide 40: Time visualization features
The expected signal amplitude
Counting alpha wave on the grids
Etc.

## Slide 41: Frequency visualization features
1/f spectral behavior
Noise harmonics
No harmonics for EEG power bands
Etc.

## Slide 42: ERP
Use the .set file (already cleaned)
EEGLAB:
Extract epochs (small segments around stimuli)
Choose the stimuli of interest
  e.g., noise vs target
Choose a baseline (e.g., -100 to 0)
Plot ERPs

## Slide 43: References
https://zeto-inc.com/blog/active-and-passive-electrodes-what-are-they-pros-cons/
Advances in Electrode Materials for Scalp, Forehead, and Ear EEG: A Mini-Review
  https://pubs.acs.org/doi/abs/10.1021/acsabm.3c00322
https://eegget-it.nl/eeg_electrodes.html
https://www.eneuro.org/content/6/2/ENEURO.0483-18.2019
https://www.mdpi.com/1424-8220/22/15/5865
https://eeglab.org/tutorials

## Slide 44: And our special thanks to those who contributed to making this workshop possible:
Maarten van Alem
Sarah Blain
Henry Brighton
Mirjam Siesling
Eva Verschoor-Suitela
Drew Hendrickson
Marijn van Wingerden
Emmanuel Keuleers